## Slide 1
 | FR (gph) | qvar | CV | UC (%)
Tape A |  |  |  | 
6 psi | 0.13 | 0.23 | 0.12 | 90.9
12 psi | 0.19 | 0.10 | 0.05 | 96.5
p-value | <.01 | 0.09 | 0.09 | 0.09
Long | 0.15 | 0.18 | 0.08 | 94.70
Short | 0.17 | 0.15 | 0.10 | 92.65
p-value | <.01 | 0.36 | 0.32 | 0.19
p-value (OP*Length) | 0.47 | 0.60 | 0.23 | 0.14
Tape B |  |  |  | 
6 psi | 0.17 | 0.09 | 0.04 | 97.0
12 psi | 0.22 | 0.09 | 0.04 | 96.8
p-value | <.01 | 0.9979 | 0.85 | 0.78
Long | 0.18 | 0.13031 | 0.049541 | 97.5764
Short | 0.20 | 0.05434 | 0.031832 | 96.3003
p-value | 0.02 | <.01 | 0.03 | 0.04
p-value (OP*Length) | 0.48 | 0.07 | 0.09 | 0.10
Tape C |  |  |  | 
6 psi | 0.16 | 0.16 | 0.08 | 94.20
12 psi | 0.25 | 0.14 | 0.07 | 94.88
p-value | <.01 | 0.50 | 0.56 | 0.57
Long | 0.18 | 0.22 | 0.09 | 92.85
Short | 0.23 | 0.09 | 0.05 | 96.23
p-value | <.01 | <.01 | <.01 | <.01
p-value (OP*Length) | 0.01 | 0.74 | 0.70 | 0.66
Table 1. Flow rates (FR) and uniformity parameters, emitter flow variation, qvar, coefficient of variation, CV and uniformity coefficient, UC for three drip tapes at 6 and 12 psi OP and two lengths of 100 ft, (short) and 300 ft (long).

## Slide 2
 | 2008 |  |  |  |  | 2009 Seasonal |  |  |  | 
 | Totaly | Total Mkt | X-L | L | M | Total | Total Mkt | X-L | L | M
Nitrogen Rate |  |  |  |  |  |  |  |  |  | 
60% | 936 | 704 | 240 | 208 | 256 | 1841b | 1586b | 683 | 493b | 410
80% | 862 | 629 | 203 | 186 | 239 | 1816b | 1553b | 664 | 459b | 430
100% | 896 | 693 | 203 | 221 | 269 | 2027a | 1761a | 716 | 566a | 479
p-value | 0.56 | 0.40 | 0.38 | 0.38 | 0.62 | 0.04 | 0.04 | 0.61 | <0.01 | 0.11
OP |  |  |  |  |  |  |  |  |  | 
6 psi | 985a | 753a | 243a | 225 | 284a | 1824 | 1563b | 641b | 472b | 450
12 psi | 811b | 598b | 188b | 185 | 225b | 1966 | 1703a | 735a | 540a | 429
p-value | <0.01 | <0.01 | 0.03 | 0.06 | 0.02 | 0.06 | 0.05 | 0.04 | <0.01 | 0.43
Irrigation |  |  |  |  |  |  |  |  |  | 
75% | 916 | 689 | 222 | 205 | 261 | 1896 | 1647 | 705 | 516 | 453
100% | 880 | 662 | 209 | 205 | 248 | 1894 | 1620 | 670 | 496 | 426
p-value | 0.51 | 0.59 | 0.60 | 0.10 | 0.61 | 0.98 | 0.70 | 0.42 | 0.42 | 0.30
p-value N*OP | 0.10 | 0.15 | 0.05 | 0.08 | 0.89 | 0.60 | 0.49 | 0.07 | 0.67 | 0.09
p-value N*IRR | 0.17 | 0.31 | 0.93 | 0.12 | 0.35 | 0.14 | 0.09 | 0.41 | <0.01 | 0.59
CV | 21.22 | 24.86 | 40.15 | 34.18 | 33.54 | 13.20 | 14.61 | 21.63 | 16.56 | 20.90
Table 2. Seasonal fresh market tomato yieldsz in number of 25-lb cartons per acre for 2008y and 2009.
z Values with different letters within the same column and under a specific treatment effect are significantly different at α=0.05 using Duncan’s multiple range test .
y Tomato yields were separated into various categories based on grading. Total: marketable and culls; Total Mkt: marketable; X-L: extra-large grade; L – large grade; M – medium grade.