## Slide 1: Ergonomic Evaluation of Scoop Shovels and Pitchforks: Impact on Women in Agriculture
Felix Oguche, Jianfeng Zhou, Karen Funkenbusch,
Marcia Shannon
FarmTechForHer
Improving Efficiency and Reducing Physical Strain through Ergonomic Design

## Slide 2: Introduction
Tools used are not designed with their unique needs in mind.
Our study aims to change that.
Chart: Number of Farms (Female-operated and All U.S.)
| Female Producers | All U.S. Producers | Female-operated Farms | All U.S. operated Farms
2012 | 969672 | 3180074 | 923945 | 2109303
2017 | 1227461 | 3399834 | 1139675 | 2042220
Every day, women farmers worldwide endure physical strain and fatigue.
1.2 million female producers
36% of U.S. farmers
Notes: Images of women farmers at work overlaid with the statistics and key figures Every day, women farmers worldwide endure physical strain and fatigue.Tools used are not designed with their unique needs in mind.
Our study aims to change that.Bringing comfort, efficiency, and safety.Empowering the hands that feed us.

## Slide 3: Objectives
Reaching, Bending, Stooping
Awkward, Positions,
Repetition
Repetition
Frequency, Strength
Focus on specific ergonomic needs of women
Evaluate shovel and pitchfork design for women farmers
Understand factors influencing MSD risks and physical strain.
Provide recommendations for tool redesign
Ensure tools are tailored to the needs of women farmers
Improved Posture
Assess the impact on body mechanics and physical strain.

## Slide 4: Methodology
24 shovels and 19 pitchforks selected
7 female participants with diverse body types
Tasks: scooping and throwing straws
AI software used for motion capture and force analysis

## Slide 5: Tool Characteristics
Handle lift height (mm)
Lift angle (degree)
Grip
Blade width (mm)
Blade thickness (mm)
Blade length (mm)
Blade Height
Handle diameter (mm)
Handle: Length, diameter, grip
dimensions.
Blade: Length, width, and thickness.
Critical: Lift angle, Handle lift height, and weight, characteristics.
SSF
PFJ
SSA
SSC
SSB
PFE
SSM
SSK
SSJ
PFL
Tool | Lift angle (degree) | Handle lift height (mm) | Weight (kg)
SSB | 56 | 781 | 1.61
PFA | 49 | 1124 | 2.00
PFE | 39 | 537 | 0.77
Notes: High-resolution images of different tools with labels showing their ergonomic features.
Close-up images of the handles and blades.

## Slide 6: Participant Profile
Demographics: Age, height, weight, body mass index (BMI).
Physical Characteristics: Overview of participants' physical attributes.

## Slide 7: Data Collection
Physiological measurements and ergonomic variables.
Digital goniometers, dynamometers, and stadiometers for standard engineering data collection.
A GoPro camera was used to capture sessions.

## Slide 8: Statistical Analysis
Univariate regressions: Joint angles and MSD risk scores.
Multivariate regressions: Combined effects of user characteristics and tool features.
Two-way ANOVA: Used to analyze differences in joint angles and MSD risk scores across different tool conditions.
Tukey Test: Post-hoc analysis to identify specific differences between groups
Chart: P_Value
| Peak.Flexion.Hip.Angle...degree. | Peak.Flexion.Left.shoulder.Angle...degree. | Peak.Flexion.Left.elbow.Angle...degree | Peak.Flexion.Neck.Angle...degree. | Peak.Flexion.Left.wrist.Angle...degree.
Univariate p-value REBA | 0.0497 | 0.00675 | 0.451 | 0.0848 | 0.304
Univariate p-value RULA | 0.00819 | 0.0186 | 0.365 | 0.114 | 0.515

## Slide 9: Tool Preferences
Chart: Pitchfork count of D-grip handles with natural inward curve
| Dgrip NNIC | Dgrip NIC
Total | 2 | 4
Chart: Shovel count of D-grip handles with natural inward curve
| Dgrip NIC | Dgrip NNIC
Total | 5 | 1
Chart: Count of Preferred Pitchfork and Shovel with D-grip handles
| Dgrip NNIC | Dgrip NIC
Total | 3 | 9
Chart: Count of Preferred Tool Types by D-grip and Straight handles
| Dgrip NIC | Dgrip NNIC | Straight H
Total | 9 | 3 | 2
Strong preference for pitchforks PFE, PFA, shovels SSA, SSB, and SSC.
D-grip handles aligning with the natural inward curve of the hand.
Images of the preferred D-grip handle.
NIC: Natural Inward Curve
NNIC: Non-Natural Inward Curve
D-grip: the natural inward
curve of the hand.
114(mm)
32(mm)
93.13 (mm)

## Slide 10: Ergonomic Factors
Significant factors: lift angle, handle lift height, mechanical advantage, tool weight.
The combined model explains 84% of the variance in user preferences.
Chart: 
| Lift angle | Handle lift height | Weight of tool × mechanical advantage | lift angle × handle lift height | lift angle × mechanical advantage | Weight of tool~ Handle lift height * Lift angle degree + Weight of participants + Effort arm + BMI + Grip Strength + Height + Resistance arm
P_value | 0.0278 | 0.0109 | 0.3386 | 0.0203 | 0.2906 | 0.03363
SSB
560
Notes: Bar graph comparing the significance of different ergonomic factors.
Highlighted images of tools with annotations pointing out ergonomic features.

## Slide 11: Physical Strain Analysis
Impact of tool design on upper body strain, particularly arms and shoulders.
MSD risk scores for Favorite shovel/Pitchfork | p-value | MSD Risk Score (%)
REBA..MSD.RISK | 0.0833 | 8.33
RULA..MSD.RISK | 0.0171 | 17.1

## Slide 12: Predictive Models
Lift Angle:
35–45-degree lift angle reduced lower back strain by 15% (p < 0.05).
Lower REBA scores, indicating decreased MSD risk.
Handle Height:
Adjustable handles decreased shoulder and upper back strain by 20% (p < 0.05).
Reduced wrist and elbow effort angles (p < 0.01).
Auxiliary Handles:
Reduced heart rate by 6 bpm (p < 0.05).
Lower energy expenditure by 0.69 KJ/kg (p < 0.01).
Increased elbow strain, highlights need for balanced design.
Subject B PFE
Subject C PFE
Subject B SSA
Subject C SSA
Notes: Insights from statistical models on ergonomic outcomes.
Emphasis on lift angle, handle lift height, and mechanical advantage.

## Slide 13: Conclusion
Key Takeaways:
Ergonomic Design: Reduces physical strain and improves efficiency.
Body Mechanics: Optimal lift angles and handle heights minimize strain.
Critical Factors: Lift angle, handle height, and mechanical advantage.
Continuous Improvement: Essential for enhancing ergonomic benefits.
Adjustable Tool
Improved Posture
Increased Efficiency
Reduce Strain
Notes: Key Takeaways:
Ergonomic Design: Reduces physical strain and improves efficiency.
Body Mechanics: Optimal lift angles and handle heights minimize strain.
User Preferences: Preference for ergonomic D-grip handles and adjustable tools.
Critical Factors: Lift angle, handle height, and mechanical advantage.
Continuous Improvement: Essential for enhancing ergonomic benefits.

## Slide 14: Recommendations
Design tools with lift angles between 27-49 degrees and handle heights 517-984 mm.
Ensure tools are adjustable and customizable for individual needs.
AI-Enhanced Posture Analysis

## Slide 15: Acknowledgments
Special thanks to the North Central Sustainable Agriculture Research & Education (SARE) for their generous support and funding.
Appreciate the National Institute for Occupational Safety and Health (NIOSH) and the United States Department of Agriculture (USDA) for their support and guidance.
Jianfeng Zhou, Karen Funkenbusch, and Marcia Shannon, University of Missouri for their mentorship and guidance.
Aaron Yoder and Central States Center for Agricultural Safety and Health at the University of Nebraska Medical Center for their support.
Thank you to the women at the University of Missouri who participated in this research study
Grateful to my colleagues for their feedback and assistance.
Jianfeng Zhou
Karen Funkenbusch
Marcia Shannon
Notes:   Visual Aid: Summary infographic highlighting key findings and recommendations. Statement: "Future research will refine ergonomic designs for better health outcomes."
  Imagine starting your day with the tools designed to ease your workload, but ending it with intense back pain and sore wrists. This is the daily reality for many women farmers using conventional tools. Our study aims to change that."