## Slide 2: Research Problem and Objectives
Problem: Traditional agricultural tools are often designed for male body sizes, causing ergonomic mismatches that increase musculoskeletal disorder (MSD) risks among women farmers.
Goal:
Develop ergonomic auxiliary handles for shovels and pitchforks tailored to women.
Objectives:
Develop ergonomically adaptive auxiliary handles
Reduce MSD risks during farm tasks
Improve comfort, posture, and ease of tool use for women farmers
Simulate
Test
Design

## Slide 3: Research Motivation & Preliminary Findings
Baseline Findings (Conventional vs Ergo)
Hip Flexion: 60° → 44°
Wrist Flexion: 79° → 47°
Energy Expenditure: 4.98 → 4.29 kJ/kg
Elbow Strain: Increased slightly (Design Trade-off)
Key Insights Driving Innovation
Rigid handles improved posture but increased elbow strain
Ergonomic improvement was offset by new joint stress
Static designs couldn't balance all biomechanical needs
Need for adjustable, adaptive, and inclusive solutions
Ergonomic Auxiliary Handle (EAHA)
Ergonomic Auxiliary Handle (EAHB)

## Slide 4: Postural and Joint Angle Comparison Across Tool Designs
+60°
(+4)
🔴
Trunk flexion > 60° Poor posture
Conventional Tool
20°-60°
(+3)
🟡
Medium trunk flexion < 60°(poor)
Ergonomic Modified Tool (EAHB)
0-20°
(+2)
🟢
More upright posture angle > 20°
Ergonomic Modified Tool (EAHA)
LIFTING
0-60°
(+2)
🟢
60-100°
🟡
(+1)
Elbow flexion angle < 60°
Elbow flexion angle (better Improved handle position)
🔴
(+2 +1)
Elbow flexion angle < 100° (increased strain)
100°+
(increased strain)
THROWING

## Slide 5: Methodology – Human-Centered Design Approach
Ergonomic Design
  Used NIC (Natural Inward Curved) grip to support neutral wrist posture
  Chose handle lift angles: 16°, 32°, 48°
Anthropometric Fit
  Based on CAESAR, BIFMA, Dreyfuss, Woodson
  Handle height: 700 - 1100 mm (adjustable in 20 mm steps)
  Grip diameter: 35 - 40 mm for women’s hand comfort
  Covers 1st - 99th percentile of female users
Prototype & Testing
  Created ErgoFlex 1, 2, 3 with adjustable features
  Posture Simulations/Lab-tested for posture (REBA/RULA) and comfort
  Improved through user feedback and motion capture analysis
Notes: 🔍 Ergonomic Design
Used NIC (Natural Inward Curved) grip to support neutral wrist posture (~12° ulnar deviation)
Chose angles: 16°, 32°, 48° to match natural scooping and lifting motion
👩‍🔧 Anthropometric Fit
Based on CAESAR, BIFMA, NASA HIDH, Dreyfuss, Woodson
Handle height: 700–1100 mm (adjustable in 20 mm steps)
Grip diameter: 35–40 mm for women’s hand comfort
Covers 1st–99th percentile of female users
🛠️ Prototype & Testing
Created ErgoFlex 1, 2, 3 with adjustable features
Lab-tested for posture (REBA/RULA) and comfort
Improved through user feedback and motion capture analysis

## Slide 6: Technical Justification - Biomechanical Optimization
NIC (Natural Inward Curved) grip keeps wrist in neutral (>12° ulnar deviation)
Based on ergonomic principle: "Bend the tool, not the wrist"
Preset ergonomic angles: 16°, 32°, and 48°
Wrist angle comparison
Flexed Wrist Neutral Wrist
NIC Handle
Reduce Strain
Radial Deviation
Flexion
Extension
Ulnar Deviation
Neutral Wrist
(+1)
🟢
0°
🔴
(+3)
< 22°

## Slide 7: Technical Justification - Mechanical Design
Castle Nut + Cotter Pin System:
Secure under vibration
Slider Clamp + Sliding Housing:
Linear Micrometer grip adjustment
Ball-Bearing Joint:
Smooth rotation, less wear
Threaded Clamp
Castle Nut
Ball-Bearing
Slider Clamp

## Slide 8: Anthropometric Basis for Design
Key Parameters:
Handle Height: Adjustable from 590 mm to 1100 mm
NIC Grip Diameter: 35 - 40 mm (women's comfort range)
Target Elbow Height: Matches 1st to 99th percentile
Ergonomic reach zone
Data Sources: CAESAR, BIFMA, Woodson, Dreyfuss
Notes: Interpretation:
The female range (1st–95th percentile) varies from 23.5″ to 36.1″, depending on source.
The male range spans from 31.9″ to 39.5″.
Designing for tool grip forward reach should accommodate approximately 30″–36″ to cover the majority of female users, and 32″–39″ for males.

## Slide 9: Design Concept
ErgoFlex-1
ErgoFlex-2
Preset lift angle
16o 32o 48o
±45o
Dual rotation support
Natural Inward Curvature (NIC) D-grip
Adjustable Height (20mm Increment)
Adjustable Height (20mm Increment)
Natural Inward Curvature (NIC) D-grip
Preset lift angle
16o 32o 48o
± 360o Rotation
Preset lift angle
16o 32o 48o
Adjustable Height (20mm Increment)
Natural Inward Curvature (NIC) D-grip
ErgoFlex-3

## Slide 10: ErgoFlex Handle Prototypes
ErgoFlex-1
ErgoFlex-2
ErgoFlex-3
Dual rotational support (±45°)
Flexible clamping system (±360° full rotation for alignment)
Ball bearing Locking system (±60° rotation both ways)
Notes: Interpretation:
The female range (1st–95th percentile) varies from 23.5″ to 36.1″, depending on source.
The male range spans from 31.9″ to 39.5″.
Designing for tool grip forward reach should accommodate approximately 30″–36″ to cover the majority of female users, and 32″–39″ for males.

## Slide 11: Results (Ergonomic Evaluation - lifting and scooping straw)
Posture Simulations Using RULA and REBA
Simulated common tasks: lifting and scooping straw
REBA score dropped from 11 → 5 with ErgoFlex
Reduced trunk and wrist strain, better elbow/shoulder alignment
Notes: Measured Results:
REBA Score: Reduced from 11 to 5 (high to medium risk)
RULA Score: Improved wrist/elbow postures
User Feedback: Reported higher comfort and control

## Slide 12: Results ( Ergonomic Evaluation-throwing straw)
Posture Simulations Using REBA
Simulated common tasks: throwing straw
REBA score increased from 10 → 11 with EASA dropped from 10 → 7 ErgoFlex
Increase elbow/shoulder alignment

## Slide 13: Discussion
NIC grip and adjustability reduce strain, improve usability
Designs inclusive of 1st - 99th percentile body sizes
Castle nut system proved durable during repetitive motion
Findings validated by REBA/RULA scores and anthropometry
Participant feedback:
  More stable grip
  Feel easier on the back
ERGOFLEX
CONVENTIONAL
EAHA
EAHB
High Elbow Load & Lateral Bending (Fixed Handle)
Moderate Elbow Load & Side Bending (Fixed Handle)
Increased Elbow Flexion & Wrist Deviation
Neutral Grip Alignment, Less Wrist Load
Reduced Side Bending & Shoulder Strain
Reduced Wrist Flexion via Rotational Joint

## Slide 14: Future Work
What’s Next?
Real-world field validation (EMG, heart rate, posture sensors)
Modular quick-adjust handle design
Smart posture-correcting feedback system
Polar H10
Field Photo

## Slide 15: Acknowledgments
North Central Sustainable Agriculture Research & Education (SARE) for their generous support and funding.
National Institute for Occupational Safety and Health (NIOSH) and the United States Department of Agriculture (USDA) for their support and guidance.
Jianfeng Zhou, Karen Funkenbusch, and Marcia Shannon, University of Missouri for their mentorship and guidance.
Aaron Yoder and Central States Center for Agricultural Safety and Health at the University of Nebraska Medical Center for their support.
Agricultural women at the University of Missouri who participated in this research study
Colleagues for their feedback and assistance.
Jianfeng Zhou
Karen Funkenbusch
Marcia Shannon
Noel Aloysius
Teng Teeh Lim
Notes:   Visual Aid: Summary infographic highlighting key findings and recommendations. Statement: "Future research will refine ergonomic designs for better health outcomes."
  Imagine starting your day with the tools designed to ease your workload, but ending it with intense back pain and sore wrists. This is the daily reality for many women farmers using conventional tools. Our study aims to change that."

## Slide 16: Thank you for your attention.
I’m happy to take any questions.
Let's revolutionize farm tools for a safer and more equitable future.
Felix Michael Oguche
PhD Student | Biological Engineering
📧 fofdt@umsystem.edu
🌐 https://farmtechforher.com
Let's talk or collaborate.