## Slide 1: Monitoring the soil water balance
Soil moisture
Soil water potential
  Shallow
  Deep
Flux (below root zone)
Groundwater levels
Applied water
Precipitation
Evapotranspiration
Infiltration rate
Soil type analysis across depths
  Evapotranspiration
  P + IRR = ET + R + DP + ΔS
  INs
  OUTs
  Storage
  Precipitation
  Irrigation
  Deep percolation
  Surface runoff
  Soil water storage
1 ft
2 ft
3 ft
4 ft
5 ft
7 ft
6 ft
Water table
Lysimeter
Monitoring well
Soil moisture probe
Soil water potential probe
Data loggers accessed at surface
***not quite to scale but close….
  Soil water balance related monitoring equipment
Irrometer

## Slide 2: Passive wick lysimeters
lysimeter – a device that measures water movement in the soil (vadose zone)
Diatomaceous earth
Plexiglass plate
Spread wick fibers
Tipping bucket gauge
Drain hole
PVC pipe routing tipping bucket to data logger at surface
Steel mesh protection
20” hanging wick
8” diameter – 24 “ long steel divergence tube
Undisturbed soil
  Design