## Slide 1: Seasonal High Tunnels 101
Joe Rowland

## Slide 2: What is a high tunnel?

## Slide 3: Establishing a Need
Establishing a need helps develop what type of high tunnel and what specifications are needed during the purchasing and installation process
Avoiding vacant tunnels

## Slide 4: Benefits to high tunnel production
Season Extension
  Early spring, late fall, and winter production
Clean fruit/plants
Protected from elements
Reduced disease pressure
Controlled growing environment
Slower to freeze, faster to thaw
4-6 degrees protection, I assume 4!
Bigger, cleaner, better quality, earlier/later in season

## Slide 5: Season Extension
What is the need?
Benefits
  Higher profit margins
  Capturing customers early in season
  Helps in a competitive marketplace
  High fruit quality
Capturing shoulder season markets
Crops
Tomato
Pepper
Cucumber
Lettuce
Greens/Spinach
Many others

## Slide 6: Exotic Crops
Crops that are unable to grow in the field
Niche market
Ginger
Turmeric
Berries, small fruits
Special needs: soil fertilizer inputs, shade cloth, irrigation, seed prep and post harvest

## Slide 7: Winter Production
Year-round harvests
Possible in all parts of NC/SC
Great for restaurants, year-round farmers markets/CSAs
Can only produce cool season crops
Limiting factors: day length, soil temperature, viable market
Special Considerations:
Management needs
Double plastic layer/blower
Row Covers
Temperature/humidity monitoring
Crop variety selection
Extending the harvest

## Slide 8: Organic Production
Reduced dependence on pesticides
  Covered space = low disease
  Spring/Winter season extension = less pests
  High fruit quality = less post harvest needs and longer shelf life
Clemson Student Organic Farm Clemson, SC

## Slide 9: Drawbacks to high tunnel production
Pollinator Exclusion
Temperature Extremes
Summer Heat
Humidity
Soil Health
Maintenance Inputs
Perimeter Weed Management
Timothy Coolong, University of Kentucky

## Slide 10: Drawbacks
Runoff – Water diverted from roof can cause drainage issues
Shading – High tunnel will cast shade potential changing field planting capacities
Grading – Top soil movement, sediment runoff
  Placement can create odd shaped fields, difficult to plant in
Cost – expensive to construct and continually manage
Worrying about the structure during extreme weather events

## Slide 11: Cost of a High Tunnel
Size, type, truss system!
Price Estimate for 30 x 72
  Low end $10,000
  High End $20,000
  Atlas Budget Plus →

## Slide 12: Cost Continued
Many outside cost not included in original purchase of kit
  Grading
  Driving sidewall post (contracting or renting equipment)
  Hired labor or contracting for installation
  Drills, Impact Drivers, Chop Saw, Reciprocating Saw, Drill Bits, Nut Drivers, Ratchets
  Materials for endwalls
  Doors

## Slide 13
E/W
N/S

## Slide 14: Site Selection
Site selection is more important than orientation!!!
Maximize the morning sun
  Why? Warm up sooner, evaporate moisture build up
Afternoon Sun
Ventilation
Irrigation Access
Level Ground
Lomax Incubator Farm Concord, NC

## Slide 16: Building Materials
Metal tubing
  Diameter ranging between ¾” to 2 ¾”
  Chain link top rail
  Square and round tubing
Baseboards and Hip Boards
  Metal, treated wood, untreated wood
Concrete
End walls
  Metal, treated wood, untreated wood
Cabin Branch Organic Farm Columbia, SC

## Slide 17
www.growingformarket.com
Side Walls:
Drop Down
Roll Up
**Tunnel Height
Dancing Pines Farm
Efland, NC
Notes: Side walls. All the differences.

## Slide 18: Height
Gothic Tunnels are typically taller than other types
Additional height may require gable vents
Taller side walls = taller tunnel height
Roof pitch will impact height
  Snow
Access to truss structure
Sierra Nevada Brewing Company Gardens Mills River, NC

## Slide 19
Puckett Greenhouses – Quonset High Tunnel
Dancing Pines Farms Efland, NC

## Slide 20: Bow Spacing
Typical bow spacing is between 4’ and 6’
  This also indicates the spacing on the side post
Decisions on bow spacing depends on production requirements, environmental concerns, and tunnel specs
  Are you accessing the truss system during production? (trellising, hanging baskets, etc…)
  Are snow load and winds a concern?
  What is the diameter/stability of steel tubing used?
Closer bow spacing increases the strength of the tunnel to withstand more weight, both from outside pressure and hanging weight inside

## Slide 21
Lomax Incubator Farm Concord, NC
6’

## Slide 22: Truss Systems
Installing a truss system is usually an “upgrade” from basic high tunnel kits
Materials can be purchased or made to install to an existing tunnel
What are the benefits?
  Lowers the cross brace for accessibility to connect trellis systems
  Increases strength
  Decreases damage risk from snow, ice and wind
Trusses can be installed on every bow OR at equal intervals throughout the tunnel

## Slide 23
www.zimmermanhightunnels.com

## Slide 24: Plastic
Most common is a single layer of plastic
Double Layer increases heat retention and reduces damage risk
Inflation works with two layers
  Requires a blower and electricity
Aged plastic has reduced light transmission
  Plant stress
  Reduced heating capacity
6 mil 4 year greenhouse plastic (UV Stable)
6 mil Infrared Anti-condensate plastic
Bubble Wrap Type
Shade cloth
Note: Most plastics should not touch PVC!

## Slide 25
Lomax Incubator Farm Concord, NC
Double plastic layer on greenhouse

## Slide 26: Wiggle Wire
Chanel used to secure plastic
Plastic is held in with curved wire that “wiggles” into place
Can be used on wood or metal
Furring strips are also common
www.growerssupply.com

## Slide 27: Endwalls
Many kits do not include material to frame out endwalls
  Framed endwalls are considered an upgrade from basic kits
Framing provides strength and increase heat retention
  Framing also provides a structure to hang doors, vents and fans if desired
Doors – range in size. Provide openings for tractors and cross ventilation
  Multiple door style options
Vents are usually installed near the peak on both ends
Fans – used as needed for increased ventilation

## Slide 28
Lomax Incubator Farm Concord, NC UNC Charlotte Botanical Garden Charlotte, NC

## Slide 29
www.nrcs.usda.gov
www.growerssupply.com

## Slide 30: Irrigation
Basics
  Drip is best
  Plants can be placed at each emitter
  Needs: pressure reducer, filter, fittings, injection system
  Over head is necessary for cover crops. Install above the maximum height of the cover crop and irrigate as needed.
  Higher pressure is needed to run these
  Suspended from trusses or bows or wobblers mounted on ground for overhead
    Depends on long term needs and management

## Slide 32: Moveable Tunnels
Tracks
Set placements
Typically, two locations
Rollers on metal tracks
Weeds can be huge issue
Sleds
Metal or wood sleds
Typically need a tractor to move
Multiple locations
Can twist during moving events
Caterpillars
Must be anchored down!!!

## Slide 33
www.gothicarchgreenhouses.com

## Slide 34: Movable Tunnels Continued
Benefits
Multiple growing locations
  Crop rotations
  Season extension
Increased soil health
Easy to disassemble and move
Drawbacks
Typically, smaller
More management requirements
Some may require additional labor
Higher risk of damage do to extreme environmental events

## Slide 35: DIY High Tunnels
Johnny’s Selected Seeds has several models available
Benders
Chain link top rail
Farmers Friend Caterpillar Tunnel
Pre bent
Cost effective
Upgrades available
Multiple lengths

## Slide 36: Increase Capacity on Small Acreage
High tunnel can support closer spacing as compared to the field
  Plants are dryer
  Trellising considerations
  Specialized irrigation schedules ** no rain or precipitation
Urban Farms
Small 1 to 2 acre operations
Increased harvest/income from the same amount of space

## Slide 37: Crop Economics
High tunnels can gross more pre square foot as compared to field production
Input cost vary from farm to farm
Tomatoes | High Tunnel | Field
Row Feet | 400 of 30” bed | 400 of 30” bed
Bed Spacing | 2 rows at 2’ spacing | 1 row at 18” spacing
Total Plants | 400 | 266
Avg Marketable Harvest | 20 lbs per plant | 10 lbs per plant
Total Marketable lbs | 8,000 | 2,660
Avg Price per lb | $2.00 | $1.75
Gross Income | $16,000 | $4,655

## Slide 39: Recommended Resources

## Slide 40: High Tunnel Hoop House Construction Guide
Different tunnel styles
Purchasing decisions
Construction Tips
Visual examples (photos)
Terminology
https://web.extension.illinois.edu/bcjmw/downloads/54183.pdf

## Slide 41: High Tunnel Crop Production Handbook
NCAT
Great for new high tunnel farmers
Detailed informative production information

## Slide 42: High Tunnel Micro-irrigation Guide
Drip and overhead systems for high tunnels
Set up diagrams and irrigation calculations
Soil information and bed prep
Rooting depth information
https://www.carolinafarmstewards.org/high-tunnel-micro-irrigation-guide/

## Slide 43: Seasonal High Tunnel Production: Organic Tomato Guide
Varieties
Economics
Production scheduling
Care and maintenance
https://www.carolinafarmstewards.org/seasonal-high-tunnel-production-organic-tomato-guide/

## Slide 44: CFSA PROGRAMS
FARM SERVICES: Technical assistance on organic production/ certification, food safety, seasonal high tunnel production, post-harvest handling, and selling into wholesale markets.
Elma C. Lomax Incubator Farm: Certified organic incubator farm in Concord, NC. That provides beginning farmers with access to land and equipment to start their own farm business. Onsite organic research program.

## Slide 45: CFSA PROGRAMS
FOOD SYSTEMS: Provide business development assistance to farmers and businesses looking to supply the local food system.
EDUCATION: Host SAC, OCLC, and the Piedmont Farm Tour
ADVOCACY: We work to change agriculture laws and regulations to benefit local and organic small and mid-sized farms.

## Slide 46: CFSA’s Consulting Services: Organic Certification
Organic Transition: guidance choosing a certifying agent and record keeping system, Q&A on NOP regulations, and records and application review.
Conservation Activity Planning (CAP-138): a farm resource inventory, identification of resource concerns and options to address them, a soil and water quality impact analysis for each option.

## Slide 47: CFSA’s Consulting Services: Production
High Tunnel Production: Help farmers identify best management practices including planting dates, varieties selection, and irrigation, soil fertility and pest management.
Good Agricultural Practices (GAP): Conduct risk assessments, identify ways to mitigate pathogen risks, review Food Safety Plans, and provide assistance preparing for an audit.

## Slide 48: Building Wholesale Capacity
This consulting program will help you:
Assess whether or not wholesale is right for you.
Decide what kind of wholesale is right for you.
Design postharvest handling strategies to maximize efficiency, food safety, and workflow.
Understand infrastructure, packaging, labeling, traceability, transporting and basic food safety norms to meet wholesale buyer requirements.

## Slide 49: CFSA Resources
  Seasonal High Tunnel Production: Organic Tomato Guide
  High Tunnel Micro-irrigation Guide
  Infrastructure Toolkit
  GAPs Manual and Videos
  Sample CAP Plan
  Organic Transition Handbook for Produce Farmers
  Organic Enterprise Budgets
  Organic Inputs and pest Control Finders
  Downloadable recordkeeping templates
  www.carolinafarmstewards.org

## Slide 50: Questions & Survey
Thank You!