## Slide 1: High Tunnel Construction
Joe Rowland

## Slide 2: CFSA’s MISSION
We help people in the Carolinas grow and eat local, organic food by advocating for fair farm and food policies, building the systems that organic family farms need to thrive, and educating communities about local, organic farming.

## Slide 3: CFSA’s VISION
Create a regional food system that is good for consumers, good for farmers and farmworkers, and good for the land.

## Slide 4: CFSA PROGRAMS
FARM SERVICES: Technical assistance on organic production/ certification, food safety, seasonal high tunnel production, post-harvest handling, and selling into wholesale markets.
Elma C. Lomax Incubator Farm: Certified organic incubator farm in Concord, NC. That provides beginning farmers with access to land and equipment to start their own farm business. Onsite organic research program.

## Slide 5: CFSA PROGRAMS
FOOD SYSTEMS: Provide business development assistance to farmers and businesses looking to supply the local food system.
EDUCATION: Host SAC, OCLC, and the Piedmont Farm Tour
ADVOCACY: We work to change agriculture laws and regulations to benefit local and organic small and mid-sized farms.

## Slide 6: What is a high tunnel?

## Slide 7: Benefits to high tunnel production
Season Extension
  Early spring, late fall, and winter production
Lower input cost as compared to greenhouses
Clean fruit/plants
Protected from elements
Reduced disease pressure
Controlled growing environment
Spring Forth Farm Hurdle Mills, NC

## Slide 8: Benefits Continued
How it can fit into your farming model
Winter Harvest
Planting/harvesting times
Coordinate planning around current time schedule
Ten Mothers Farm Hillsborough, NC

## Slide 9: Drawbacks to high tunnel production
Pollinator Exclusion
Temperature Extremes
Summer Heat
Humidity
Soil Health
Maintenance Inputs
Perimeter Weed Management
Timothy Coolong, University of Kentucky

## Slide 10: Drawback Continued
Runoff – Water diverted from roof can cause drainage issues
Shading – High tunnel will cast shade potential changing field planting capacities
Grading – Top soil movement, sediment runoff
  Placement can create odd shaped fields, difficult to plant in
Cost – expensive to construct and continually manage
Worrying about the structure during extreme weather events

## Slide 11: Cost of a High Tunnel
Size, type, truss system!
Price Estimate for 30 x 72
  Low end $10,000
  High End $20,000
  Atlas Budget Plus →

## Slide 12: Cost Continued
Many outside cost no included in original purchase of kit
  Grading
  Driving sidewall post (contracting or renting equipment)
  Hired labor or contracting for installation
  Drills, Impact Drivers, Chop Saw, Reciprocating Saw, Drill Bits, Nut Drivers, Ratchets
  Materials for endwalls
  Doors

## Slide 13: NRCS EQIP
Natural Resources Conservation Service : Environmental Quality Incentives Program
Provides Cost Share to help conduct practices to preserve natural resources and increase environmental health which includes high tunnels
Applications due in November and are approved yearly
The grower pays upfront and if reimbursed based on high tunnel square footage after the tunnel in constructed

## Slide 14: Other Funding Options
Slow Money Institute www.slowmoney.org
Kiva Loans www.kiva.org
Local Grants
  These vary depending on your area
  Most are small amounts
Loans
  NC Farm Credit
  Farm Bureau
  AgSouth Farm Credit
Chickadee Farm Clayton, NC

## Slide 15: Orientation
Maximizing angle and exposure to sunlight
Capitalizing on greenhouse effect to gain and retain warmth
Avoid shading within the tunnel
Most recommendations hinge on latitude

## Slide 16
E/W
N/S

## Slide 17: Site Selection
Site selection is more important than orientation!!!
Maximize the morning sun
  Why?
Afternoon Sun
Ventilation
Irrigation Access
Level Ground
Lomax Incubator Farm Concord, NC

## Slide 18: Size Options
Single Bay
  Most used sizes are 30’ x 72’ and 30’ 96’
  Repurposed cold frames are typically thinner 15’ x 20-150’
Multi Bay
  Multiple single bays put together
  Gutter connect
  Benefits and drawbacks
DIY
  Farmers Friend
  Johnny's Selected Seeds Models
Johnny’s Stationary Gothic Peak Model

## Slide 20: Building Materials
Metal tubing
  Diameter ranging between ¾” to 2 ¾”
  Chain link top rail
  Square and round tubing
Baseboards and Hip Boards
  Metal, treated wood, untreated wood
Concrete
End walls
  Metal, treated wood, untreated wood
Cabin Branch Organic Farm Columbia, SC

## Slide 21: Side Walls
Curved vs straight
Burying post/soil types
Roll Up vs Drop Down
Curtains material
Pockets vs No pockets
  Seal of the tunnel during cold events
  Air in and out during high winds
Johnny’s Stationary Elliptical Model

## Slide 22
www.growingformarket.com
The Farm at Penny Lane Pittsboro, NC

## Slide 23: Height
Gothic Tunnels are typically taller then other types
Additional height may require gable vents
Taller side walls = taller tunnel height
Roof pitch will impact height
  Snow
Access to truss structure
Equipment Access
Sierra Nevada Brewing Company Gardens Mills River, NC

## Slide 24: Tunnel Style
Gothic
Quonset Hut
Ridge vent
Gutter Connect
Morgan County Seeds – Gothic High Tunnel

## Slide 25
Puckett Greenhouses – Quonset High Tunnel
Dancing Pines Farms Efland, NC

## Slide 26
Four Season Tools
www.extension.org

## Slide 27
http://missouribeginningfarming.blogspot.com
Maters and More Mt Pleasant, NC

## Slide 28
Atlas Greenhouses – Gutter Connect

## Slide 29: Bow Spacing
Typical bow spacing is between 4’ and 6’
  This also indicates the spacing on the side post
Decisions on bow spacing depends on production requirements, environmental concerns, and tunnel specs
  Are you accessing the truss system during production? (trellising, hanging baskets, etc…)
  Are snow load and winds a concern?
  What is the diameter/stability of steel tubing used?
Closer bow spacing increases the strength of the tunnel to withstand more weight, both from outside pressure and hanging weight inside

## Slide 30
Lomax Incubator Farm Concord, NC
6’

## Slide 31: Truss Systems
Installing a truss system is usually an “upgrade” from basic high tunnel kits
Materials can be purchased or made to install to an existing tunnel
What are the benefits?
  Lowers the cross brace for accessibility to connect trellis systems
  Increases strength
  Decreases damage risk from snow, ice and wind
Trusses can be installed on every bow OR at equal intervals throughout the tunnel

## Slide 32
www.zimmermanhightunnels.com

## Slide 33: Plastic
Most common is a single layer or plastic
Double Layer increases heat retention and reduces damage risk
Inflation works with two layers
  Requires a blower and electricity
Aged plastic has reduced light transmission
  Plant stress
  Reduced heating capacity
6 mil 4 year greenhouse plastic
6 mil Infrared Anti-condensate plastic
Shade cloth
Note: Most plastics should not touch PVC!

## Slide 34
Lomax Incubator Farm Concord, NC
Double plastic layer on greenhouse

## Slide 35: Wiggle Wire
Chanel used to secure plastic
Plastic is held in with curved wire that “wiggles” into place
Can be used on wood or metal
Furring strips are also common
www.growerssupply.com

## Slide 36: Endwalls
Many kits do not include material to frame out endwalls
  Framed endwalls are considered an upgrade from basic kits
Framing provides strength and increase heat retention
  Framing also provides a structure to hang doors, vents and fans if desired
Doors – range in size. Provide openings for tractors and cross ventilation
  Multiple door style options
Vents are usually installed near the peak on both ends
Fans – used as needed for increased ventilation

## Slide 37
Lomax Incubator Farm Concord, NC UNC Charlotte Botanical Garden Charlotte, NC

## Slide 38
www.nrcs.usda.gov
www.growerssupply.com

## Slide 39: Endwalls continued
Plastic
  Inflation
Polycarbonate
www.atlasgreehouses.com

## Slide 40: Irrigation
Basics
  Drip is best
  Plants can be placed at each emitter
  Needs: pressure reducer, filter, fittings, injection system
  Over head is necessary for cover crops. Install above the maximum height of the cover crop and irrigate as needed.
  Higher pressure is needed to run these

## Slide 42: Moveable Tunnels
Tracks
Set placements
Typically two locations
Rollers on metal tracks
Weeds can be huge issue
Sleds
Metal or wood sleds
Typically need a tractor to move
Multiple locations
Can twist during moving events
Must be anchored down!!!

## Slide 43
www.gothicarchgreenhouses.com

## Slide 44: Movable Tunnels Continued
Benefits
Multiple growing locations
  Crop rotations
  Season extension
Increased soil health
Easy to disassemble and move
Drawbacks
Typically, smaller
More management requirements
Some may require additional labor
Higher risk or damage do to extreme environmental events

## Slide 45: DIY High Tunnels
Johnny’s Selected Seeds has several models available
Benders
Chain link top rail
Farmers Friend Caterpillar Tunnel
Pre bent
Cost effective
Upgrades available
Multiple lengths

## Slide 46: Multiple Tunnels
Clemson Student Organic Farm Clemson, SC

## Slide 47: List of Suppliers
Carolina Greenhouses – Kinston, NC
Farm Tek (Grow Span Structures) - Dyersville, IA
Jaderloon (The Greenhouse Company) – Columbia, SC
Nolt’s Greenhouse Supplies – Ephrata, PA
Tunnel Vision Hoops - Shaker Heights, OH
Atlas Greenhouses – Alapaha, GA
Puckett Greenhouse – Ararat, VA
Berry Hill Irrigation – Buffalo Junction, VA
Rimol Greenhouse Systems – Hooksett, NH
Farmer’s Friend – Centerville, TN
Williamson Greenhouses – Clinton, NC
Morgan County Seed – Barnett, Missouri
Four Season Tools – Kansas City, Missouri
Zimmerman Greenhouses – Versailles, Missouri
A more comprehensive list on www.hightunnels.org

## Slide 48: CFSA’s Consulting Services: Organic Certification
Organic Transition: guidance choosing a certifying agent and record keeping system, Q&A on NOP regulations, and records and application review.
Conservation Activity Planning (CAP-138): a farm resource inventory, identification of resource concerns and options to address them, a soil and water quality impact analysis for each option.

## Slide 49: CFSA’s Consulting Services: Production
High Tunnel Production: Help farmers identify best management practices including planting dates, varieties selection, and irrigation, soil fertility and pest management.
Good Agricultural Practices (GAP): Conduct risk assessments, identify ways to mitigate pathogen risks, review Food Safety Plans, and provide assistance preparing for an audit.

## Slide 50: CFSA’s Consulting Services: Wholesale Readiness
Building Wholesale Capacity:
Help farmers assess wholesale readiness and understand post-harvest handling infrastructure, packaging, labeling, traceability, transportation and basic food safety norms to meet wholesale requirements

## Slide 51: CFSA Resources
  Seasonal High Tunnel Production: Organic Tomato Guide
  High Tunnel Micro-irrigation Guide
  Infrastructure Toolkit
  GAPs Manual and Videos
  Sample CAP Plan
  Organic Transition Handbook for Produce Farmers
  Organic Enterprise Budgets
  Organic Inputs and pest Control Finders
  Downloadable recordkeeping templates
  www.carolinafarmstewards.org

## Slide 52: Questions & Survey
Thank You!