## Slide 1
Classifying Aflatoxin B1-Contaminated Peanut Seeds Using Hyperspectral Imaging with Machine Learning
Md Tauhidul Alam1, Jake Fountain1, Harald Scherm1, Md Sultan Mahmud1, Christopher Kucha2
1Department of Plant Pathology, University of Georgia
2Department of Food Science & Technology, University of Georgia

## Slide 2
Introduction: Peanut Industry and Aflatoxin Issue
Georgia produces more than 50% of peanut grown in the USA[1]
A $2.2 billion peanut industry in Georgia[1]
Aflatoxin produced by Aspergillus flavus and Aspergillus parasiticus
Affect vital organs
In 2019, 126 million losses due to the rejection of 30% shelled runner peanuts in the southeastern U.S.[2]
1 Georgia Peanut Commission. Georgia Peanut Commission. Available from: https://gapeanuts.com/about/.
2 Butts, C., et al., US peanut quality: Industry priorities to mitigate aflatoxin risk from farm to consumer. Peanut Science, 2023. 50(1): p. 29–40.
Fig. Health impacts of Aflatoxin
Aspergillus spp.
Infected Peanuts
AFB1
Immune Suppression
Stunt Growth
Aflatoxicosis
Liver Cancer
2

## Slide 3
Introduction: Contaminated Peanut Identification and Limitations
Shelled Peanut Lot
20 MT 20 MT
Aggregate Sample 70-75 kg
Sample 1
22kg
Sample 2
22kg
Sample 3
22kg
1100 g
1100 g
1100 g
1A
2B
1B
2A
3A
3B
20 ppb
20 ppb
20 ppb
5000 ppb
10000 ppb
0ppb
0ppb
10000 ppb
Seg. III Peanuts - Perception (Uniform Contamination)
Seg. III Peanuts - Reality (Heterogenous Contamination)
Aflatoxin contamination in peanuts is extremely uneven
A few bad peanuts can be scattered among thousands of good ones
Sampling system can easily miss contaminated kernels or wrongly classify a good lot as bad (due to small sample size)
Seg. I Peanuts (0 ppb)
3
Notes: Shelled peanut lot sizes in US commerce are typically 20 metric tons (MT) form which 70-75 kg sample is collected and divided into three independent 22 kg samples for sequential aflatoxin testing (Davis et al., 2018). From each 22 kg sample, 1100 grams is collected and divided into two subsamples (A and B) for duplicate chemical analysis

## Slide 4
Introduction: Methods of Aflatoxin Detection and Limitations
Slow, destructive, and expensive, requiring milling, chemical extraction, and lab analysis
Because only a tiny fraction of kernels are actually tested, even a well‑designed sampling program cannot guarantee that every contaminated peanut is caught
Industry demand fast, automated, non‑destructive methods to scan each kernel directly and rapidly
ELISA
HPLC
Gas Chromatography
AFB1
4

## Slide 5
Introduction: Hyperspectral Imaging and It’s Potential
RGB is suitable for detecting moldy, discolored and damaged peanuts
RGB not suitable for detecting asymptomatic aflatoxin-contaminated peanuts
Hyperspectral imaging (HSI) has potential to identify both symptomatic and asymptomatic contaminated peanuts
400 nm
700 nm
Visible light
400 nm
700 nm
Visible light
1700 nm
Near Infrared
HSI cameras
RGB cameras
5

## Slide 6
Goal and Objectives
Goal: Develop an autonomous screening system capable of distinguishing and separating each aflatoxin-contaminated peanut from non-contaminated ones reliably and rapidly
Specific Objectives:
Artificially contaminate peanuts with aflatoxin B1 to obtain controlled contamination levels for experimental samples
Identify important hyperspectral imaging wavelengths sensitive to aflatoxin contamination to reduce data processing time and improve detection performance
Use machine learning models with identified important wavelengths to distinguish contaminated peanuts with 10,000 ppb aflatoxin B1 from non-contaminated peanuts treated with 70% methanol
6

## Slide 7
10,000 ppb AFB1 (Cat. No. A6636, Sigma-Aldrich, USA)
70% methanol (control)
Camera: 400-1000 nm
Halogen light (50 watt):400-2000
Conveyor plate
Camera: 900-1700 nm
Image acquisition with hyperspectral imaging system
5 µL of 10,000 ppb AFB1 applied to each peanut using a micropipette
Seeds were dried in for 2.5 hours
5 µL of 70% methanol applied to each peanut using a micropipette
Georgia-06 peanuts with uniform size and no visible damage
Peanut kernels were cut in half using a scalpel

## Slide 8: Methodology: Data Processing and Classification Workflow
Raw Image
RGB Image
Mean Spectra
Image Annotation
PLS-DA
LDA
Logistic Regression
Support Vector Regression
Comminated
Machine Learning Models
Non contaminated
CARS
Identifying important Wavelengths
8

## Slide 9: Results: Mean Spectra
900
989
1169
1079
1527
1258
1348
1438
1700
1617
Wavelengths (nm)
0.85
0.80
0.75
0.70
0.65
0.60
0.55
0.90
0.95
Mean Intensity
400
467
601
534
870
669
736
803
1000
938
Wavelengths (nm)
0.8
0.7
0.6
0.5
0.4
0.3
0.2
0.9
Mean Intensity
0 ppb
10,000 ppb
0 ppb
10,000 ppb
Near-Infrared (NIR) Reflectance (900 – 1800 nm)
Visible Near-Infrared (VNIR) Reflectance (400 nm – 1000 nm)
Showing differences between 0 ppb and 10,000 ppb in HSI spectra
Notes: Write how you will explain

## Slide 10
Results: Feature Selection Using CARS
VNIR Data Annotation
(a)
(b)
(c)
Fig. (a) shows the progression of feature elimination using Monte Carlo sampling. The number of wavelengths decreases and stabilizes around 210 runs, indicating the optimal feature set.
Fig (b) shows that RMSECV reaches its minimum between 214 to 225 runs, confirming the best model performance at this point.
Fig. (c) illustrates that regression coefficients stabilize near 214 runs, revealing the key wavelengths selected by CARS.
Data Source | Selected Wavelengths (CARS)
VNIR | 22 bands
NIR | 23 bands
Fused Spectral Data (VNIR and NIR) | 41 bands
10
350
0
50
150
100
200
250
300
350
400
450
500
0
50
150
100
200
250
300
400
Number of sampling runs
Number of sampled variables
0.35
0.4
0.5
0
50
150
100
200
250
300
350
400
450
500
0.45
Number of sampling runs
RMSECV
-150
-100
0
-50
50
100
150
0
50
150
100
200
250
300
350
400
450
500
Number of sampling runs
Regression coefficients path
Notes: Write how you will explain

## Slide 11
Results: Classification Results
Chart: 
| PLS-DA | LDA | Logistic Regression | Support Vector Regression
 | 0.7749 | 0.7792 | 0.7835 | 0.7835
Chart: 
| PLS-DA | LDA | Logistic Regression | Support Vector Regression
 | 0.8442 | 0.8485 | 0.8528 | 0.8485
NIR Data
Chart: 
| PLS-DA | LDA | Logistic Regression | Support Vector Regression
 | 0.8528 | 0.8745 | 0.8571 | 0.8788
Fused Spectral Data
Four algorithms were used for classification: Partial Least Squares Discriminant Analysis (PLS-DA), Linear Discriminant Analysis (LDA), Support Vector Regressor (SVR), and Logistic Regression
Machine learning models learn patterns from peanut spectral data to distinguish contaminated and non-contaminated kernels
11
Notes: How ML works

## Slide 12
Summary and Future Directions
VNIR Data Annotation
CARS outperformed Principal Component Analysis (PCA) because it directly selects the most informative wavelengths related to aflatoxin contamination.
Forty-one key wavelengths from combined dataset showed strong potential for differentiating highly contaminated peanuts from non-contaminated kernels
Support Vector Regression (SVR) achieved the highest classification accuracy (87.88%) for distinguishing 0 and 10,000 ppb aflatoxin B1 contamination levels
Validate selected key wavelengths and models using naturally contaminated peanut samples
12

## Slide 13
Acknowledgements
Dr. Jake Fountain
Dr. Harald Scherm
Dr. Md Sultan Mahmud
Dr. Christopher Kucha
Dr. Marin Brewer
Dr. Shavannor Smith
Ms. Lorna Nissen
Lab Members from Drs. Smith, Fountain and Mahmud Lab
Grant No. GS25-332
13

## Slide 14
Thank You
Contact: MdTauhidul.Alam@uga.edu (T. Alam)