## Slide 1: Synthesis of Thiophene and Thiolane Derivatives Found in Biodiesel Produced from Brown Grease Lipids
By
Isah Shehu
07/25/2019

## Slide 2: Outline of Presentation
Synthesis of Methyl 8-(2’,5’-hexylthienyl)octanoate (1)
Synthesis of epithiostearate (2)
Synthesis of cross-linked disulfide (3)
Synthesis of cross-linked sulfide (4)
Synthesis of epidithiostearate (5)
Synthesis of 5-butyl dihydrthiophen-2-one (6)

## Slide 3: Synthesis of Methyl 8-(2’,5’-hexylthienyl)octanoate (1)
The synthesis is according to the procedure described by Gunstone et al., (1973) with some modifications. The multi-step synthesis is shown in scheme 1.

## Slide 4: Synthesis of Methyl 8-(2’,5’-hexylthienyl)octanoate (1)
Modification:
Henbest Reduction: toluene @ 110 OC and use of Dean Trap Distillation
  Modified Solvent from Ethylene Glycol to Toluene to easier work up. Product was soluble in Ethylene Glycol.
Caglioti Reduction: synthesis and reduction of tosyl hydrazine (Bouhadir et al (2012); Hutchins et al (1973).
Scheme 2: Caglioti Reduction: Synthesis and reduction of tosyl hydrazone

## Slide 5: Synthesis of Methyl 8-(2’,5’-hexylthienyl)octanoate (1)
Scheme 3: Caglioti reaction (Hydrazone reduction) over 24 hr

## Slide 6: Scheme 1. Intermediate #1
MM 182 g/mol
C-Detector
S-Detector
MM 182g/mol

## Slide 7: Scheme 1. Intermediate #2
C-Detector
S-Detector
168g
MM 168g/mol

## Slide 8: Scheme 1. Intermediate #3
MW: 338 g/mol
MW: 338 g/mol
C-Detector
S-Detector

## Slide 9: Preparative Separation of Reaction Products
TLC
Thin layer chromatograms (TLC) were carried out on glass support silica gel 60 plates (0.25 mm layer, F-254) (E.Merck No. 5765) and developed using varied solvent mixtures as follows.
n-hexane (100 %);
n-hexane: ethyl acetate: acetic acid (80:20:1);
n-hexane:ethyl acetate (90:10):
n-hexane:ethyl acetate (95:5);
n-hexane: ethyl acetate (99:1);
n-hexane:diethyl ether (95:5) and
n-hexane:diethyl ether (99:1).
Short column Chromatography
A suitable solvent system is chosen from the results of analytical TLC with acceptable ∆Rf for product separation
20 mm x 5 in column of 10 g of silica gel 60 for sample loading of 1 g each and solvent elution of 10 ml, 5 ml or 2 ml
Conditioned with 2 x 10 ml of appropriate solvent before application of sample. Elution carried out under gravity except on rare occasions were vacuum pressure is applied for effective elution.
The last component is usually flushed using either diethyl ether or ethyl acetate

## Slide 10: Gunstone Reaction Unsuccessful
C-Detector
SW-Detector
MW: 324 g/mol

## Slide 11: Methyl 8-(2’,5’-hexylthienyl)octanoate (1) via Caglioti Reaction
C-Detector
S-Detector

## Slide 12: Synthesis of Epithiostearate (2) The synthesis is according to the procedure described by Gunstone et al., (1973) with some modifications. The multi-step synthesis is shown in scheme 1a.
This proposed procedure was abandoned due to the unsuccessful attempts to synthesis target #1

## Slide 13: Synthesis of Epithiostearate (2)
Scheme 4a. Via Caglioti reduction (Hutchins et al., 1973):
Scheme 4b. Via Methylsulfonyl (mesyl) ester (Gunstone et al., 1973);
(Gunstone intermediate)
(from Oxy-mercuration and
de-mercuration of Methyl-Ricinoleate

## Slide 14: Methyl 9, 12-Epithiostearate (2)
C-Detector
S-Detector

## Slide 15: Scheme 5. Synthesis of cross-linked disulfide (3) from methyl 12-hydroxystearate
Me 12-hydroxystearate
(1:2)
(1:10)
3, 10%

## Slide 16: Cross-linked Disulfide
C-Detector
S-Detector

## Slide 17: Scheme 6. Synthesis of Cross-linked Sulfide (4)

## Slide 18: Crossed-linked Sulfide
C-Dtector
S-Detector

## Slide 19: Scheme 6 :Methyl 10,12-epidithiostearate (5) obtained from treating the corresponding mesylate ester (D) with excess NaHS.

## Slide 20: Epidithiosterate
S-Detector

## Slide 21: Synthesis of 5-butyl dihydrothiophen-2-one (6)

## Slide 22: 5-butyl dihydrothiophen-2-one (6)

## Slide 23: Results
Mass spectra